## Slide 1
MEMS based Machine Vibration Monitoring and Management System
TEAM – 6
23BME007 - AKSHAI U
23BME016 - DEENADHAYALAN B
23BME017 - DEEPAK PRASANNA S M
23BME046 - KEERTHIN P
23BME053 - MITHRANN S S
23BME055 - NAREN K
Smart Monitoring for Safer Machines
System Architecture Overview
ESP32 Controller
Main processor with WiFi, Bluetooth, and I/O support.
ADXL345 Accelerometer
3-axis MEMS sensor capturing real-time vibration and acceleration data.
LCD Display
Local status and live vibration readings with calibration prompts.
GSM Module
SIM800 sends SMS alerts for excessive vibration events instantly.
Problem Statement
It is found from a study that machines often experience problems when they face prolonged vibrations. These vibrations make parts wear out faster, cause breakdowns, create noise, and reduce the quality of work.
This leads to unexpected stoppages, higher repair costs, and lower efficiency, showing the need for a reliable system to track machine vibrations.

## Slide 2
MEMS based Machine Vibration Monitoring and Management System
TEAM – 6
23BME007 - AKSHAI U
23BME016 - DEENADHAYALAN B
23BME017 - DEEPAK PRASANNA S M
23BME046 - KEERTHIN P
23BME053 - MITHRANN S S
23BME055 - NAREN K
Smart Monitoring for Safer Machines
Problem Statement
ESP32 Controller
Main processor with WiFi, Bluetooth, and I/O support.
ADXL345 Accelerometer
3-axis MEMS sensor capturing real-time vibration and acceleration data.
LCD Display
Local status and live vibration readings with calibration prompts.
GSM Module
SIM800 sends SMS alerts for excessive vibration events instantly.
Hardware Architecture
It is found from a study that machines often experience problems when they face prolonged vibrations. These vibrations make parts wear out faster, cause breakdowns, create noise, and reduce the quality of work.
This leads to unexpected stoppages, higher repair costs, and lower efficiency, showing the need for a reliable system to track machine vibrations.
Wireless Data Logging and Alert System
    The module can wirelessly store the vibration data in the BLYNK WEB CONSOLE and also generate a sound based alert when the vibration exceeds the threshold
  Auto Calibration
    The module calibrates the threshold value of vibration beyond which an alarm should be triggered automatically
MEMS based Machine Vibration Monitoring and Management System that can measure vibration and wirelessly log data along with alerts for high vibration
Continuous and Real Time Sensing
    ADXL345 measures even the minute fluctuations in vibrations and the ESP32 module process these values to get its equivalent vibration measurement in real time.
Our Solution

## Slide 3
MEMS based Machine Vibration Monitoring and Management System
TEAM – 6
23BME007 - AKSHAI U
23BME016 - DEENADHAYALAN B
23BME017 - DEEPAK PRASANNA S M
23BME046 - KEERTHIN P
23BME053 - MITHRANN S S
23BME055 - NAREN K
Smart Monitoring for Safer Machines
Problem Statement
ESP32 Controller
Main processor with WiFi, Bluetooth, and I/O support.
ADXL345 Accelerometer
3-axis MEMS sensor capturing real-time vibration and acceleration data.
LCD Display
Local status and live vibration readings with calibration prompts.
GSM Module
SIM800 sends SMS alerts for excessive vibration events instantly.
Hardware Architecture
It is found from a study that machines often experience problems when they face prolonged vibrations. These vibrations make parts wear out faster, cause breakdowns, create noise, and reduce the quality of work.
This leads to unexpected stoppages, higher repair costs, and lower efficiency, showing the need for a reliable system to track machine vibrations.
Wireless Data Logging and Alert System
    The module can wirelessly store the vibration data in the BLYNK WEB CONSOLE and also generate a sound based alert when the vibration exceeds the threshold
  Auto Calibration
    The module calibrates the threshold value of vibration beyond which an alarm should be triggered automatically
MEMS based Machine Vibration Monitoring and Management System that can measure vibration and wirelessly log data along with alerts for high vibration
Continuous and Real Time Sensing
    ADXL345 measures even the minute fluctuations in vibrations and the ESP32 module process these values to get its equivalent vibration measurement in real time.
Our Solution

## Slide 4
MEMS based Machine Vibration Monitoring and Management System
TEAM – 6
23BME007 - AKSHAI U
23BME016 - DEENADHAYALAN B
23BME017 - DEEPAK PRASANNA S M
23BME046 - KEERTHIN P
23BME053 - MITHRANN S S
23BME055 - NAREN K
Smart Monitoring for Safer Machines
Hardware Architecture
ESP32 Controller
Main processor with WiFi, Bluetooth, and I/O support.
ADXL345 Accelerometer
3-axis MEMS sensor capturing real-time vibration and acceleration data.
LCD Display
Local status and live vibration readings with calibration prompts.
GSM Module
SIM800 sends SMS alerts for excessive vibration events instantly.
Wireless Data Logging and Alert System
    The module can wirelessly store the vibration data in the BLYNK WEB CONSOLE and also generate a sound based alert when the vibration exceeds the threshold
  Auto Calibration
    The module calibrates the threshold value of vibration beyond which an alarm should be triggered automatically
MEMS based Machine Vibration Monitoring and Management System that can measure vibration and wirelessly log data along with alerts for high vibration
Continuous and Real Time Sensing
    ADXL345 measures even the minute fluctuations in vibrations and the ESP32 module process these values to get its equivalent vibration measurement in real time.
Our Solution
Real time representation of axis, vibration and the threshold values in Arduino IDE serial monitor
REAL TIME REPRESENTATION OF AXIS, VALUES in Blynk Console along with Alarm on excessive vibrations being detected
SOFTWARE IMPLEMENTATION

## Slide 5
System Architecture Overview
ESP32 Controller
Main processor with WiFi, Bluetooth, and I/O support.
ADXL345 Accelerometer
3-axis MEMS sensor capturing real-time vibration and acceleration data.
LCD Display
Local status and live vibration readings with calibration prompts.
GSM Module
SIM800 sends SMS alerts for excessive vibration events instantly.
Real time representation of axis, vibration and the threshold values in Arduino IDE serial monitor
REAL TIME REPRESENTATION OF AXIS, VALUES in Blynk Console along with Alarm on excessive vibrations being detected
SOFTWARE IMPLEMENTATION
Device Startup
LCD shows status and connection messages.
WiFi connects to Blynk; GSM module initializes.
Calibration
User presses boot button to calibrate at any time.
Baseline offsets and thresholds computed.
Monitoring
Calibrated sensor data is streamed and visualized (V0=X, V1=Y, V2=Z, V3=Vibration).
LCD displays real-time vibration frequency.
Alert and Logging
Dashboard alerts trigger on excessive vibration.
Status and history maintained for remote monitoring.
Manual Recalibration
Boot button allows recalibration during normal operation.
LIVE DEMO : Workflow & Operation

## Slide 6
System Architecture Overview
ESP32 Controller
Main processor with WiFi, Bluetooth, and I/O support.
ADXL345 Accelerometer
3-axis MEMS sensor capturing real-time vibration and acceleration data.
LCD Display
Local status and live vibration readings with calibration prompts.
GSM Module
SIM800 sends SMS alerts for excessive vibration events instantly.
Real time representation of axis, vibration and the threshold values in Arduino IDE serial monitor
REAL TIME REPRESENTATION OF AXIS, VALUES in Blynk Console along with Alarm on excessive vibrations being detected
SOFTWARE IMPLEMENTATION
Device Startup
LCD shows status and connection messages.
WiFi connects to Blynk; GSM module initializes.
Calibration
User presses boot button to calibrate at any time.
Baseline offsets and thresholds computed.
Monitoring
Calibrated sensor data is streamed and visualized (V0=X, V1=Y, V2=Z, V3=Vibration).
LCD displays real-time vibration frequency.
Alert and Logging
Dashboard alerts trigger on excessive vibration.
Status and history maintained for remote monitoring.
Manual Recalibration
Boot button allows recalibration during normal operation.
LIVE DEMO : Workflow & Operation
Affordable Solution
Open-source hardware and cloud platforms reduce monitoring costs significantly.
Predictive Maintenance
Early vibration detection prevents equipment failure and reduces downtime.
Real-Time Insights
Continuous monitoring provides actionable data for maintenance decisions.

## Slide 7
System Architecture Overview
ESP32 Controller
Main processor with WiFi, Bluetooth, and I/O support.
ADXL345 Accelerometer
3-axis MEMS sensor capturing real-time vibration and acceleration data.
LCD Display
Local status and live vibration readings with calibration prompts.
GSM Module
SIM800 sends SMS alerts for excessive vibration events instantly.
Real time representation of axis, vibration and the threshold values in Arduino IDE serial monitor
REAL TIME REPRESENTATION OF AXIS, VALUES in Blynk Console along with Alarm on excessive vibrations being detected
SOFTWARE IMPLEMENTATION
Device Startup
LCD shows status and connection messages.
WiFi connects to Blynk; GSM module initializes.
Calibration
User presses boot button to calibrate at any time.
Baseline offsets and thresholds computed.
Monitoring
Calibrated sensor data is streamed and visualized (V0=X, V1=Y, V2=Z, V3=Vibration).
LCD displays real-time vibration frequency.
Alert and Logging
Dashboard alerts trigger on excessive vibration.
Status and history maintained for remote monitoring.
Manual Recalibration
Boot button allows recalibration during normal operation.
LIVE DEMO : Workflow & Operation
Affordable Solution
Open-source hardware and cloud platforms reduce monitoring costs significantly.
Predictive Maintenance
Early vibration detection prevents equipment failure and reduces downtime.
Real-Time Insights
Continuous monitoring provides actionable data for maintenance decisions.
RESULTS AND POSITIVE IMPACTS

## Slide 8
Multi-Sensor Expansion
Add temperature, humidity, and acoustic sensors for comprehensive machine health monitoring.
Data Logging
Store historical vibration data for long-term trend analysis and pattern recognition.
System Architecture Overview
ESP32 Controller
Main processor with WiFi, Bluetooth, and I/O support.
ADXL345 Accelerometer
3-axis MEMS sensor capturing real-time vibration and acceleration data.
LCD Display
Local status and live vibration readings with calibration prompts.
GSM Module
SIM800 sends SMS alerts for excessive vibration events instantly.
Real time representation of axis, vibration and the threshold values in Arduino IDE serial monitor
REAL TIME REPRESENTATION OF AXIS, VALUES in Blynk Console along with Alarm on excessive vibrations being detected
SOFTWARE IMPLEMENTATION
Device Startup
LCD shows status and connection messages.
WiFi connects to Blynk; GSM module initializes.
Calibration
User presses boot button to calibrate at any time.
Baseline offsets and thresholds computed.
Monitoring
Calibrated sensor data is streamed and visualized (V0=X, V1=Y, V2=Z, V3=Vibration).
LCD displays real-time vibration frequency.
Alert and Logging
Dashboard alerts trigger on excessive vibration.
Status and history maintained for remote monitoring.
Manual Recalibration
Boot button allows recalibration during normal operation.
LIVE DEMO : Workflow & Operation
Affordable Solution
Open-source hardware and cloud platforms reduce monitoring costs significantly.
Predictive Maintenance
Early vibration detection prevents equipment failure and reduces downtime.
Real-Time Insights
Continuous monitoring provides actionable data for maintenance decisions.
RESULTS AND POSITIVE IMPACTS
Future Enhancements
AI Analytics
Machine learning models predict equipment failures before they occur.
Enhanced Visualization
Advanced dashboard with 3D vibration mapping and comparative analytics across machinery fleet.